## Slide 1: Toxicology Drug Testing and trends
Sara J. Schreiber, PhD, D-abft
WATCP - October 2024

## Slide 2: A quick get to know ya

## Slide 3: Matrices for screening
Blood
Urine
Oral Fluid
Hair

## Slide 4: Drug detection times
Breath < Blood ~ Oral Fluid < Urine < sweat < hair

## Slide 5: Benefits and drawbacks of blood
Actively circulating
Current snapshot
Most data for this matrix
Not easily adulterated
Skilled collection
Invasive collection

## Slide 6: Benefits and drawbacks of urine
Provides Historical information
Metabolite heavy
Uninterpretable concentrations
Specimen collection issues
Adulteration issues

## Slide 7: Oral Fluid Drug Testing

## Slide 8: Oral fluid
Oral fluid
  Water, Electrolytes, immunoglobins, Enzymes, Proteins
  Normal ph: 5.5-7.9, Normal flow is variable
    PH and flow rate is variable based on
      Circadian rhythms, physical activity and health
    Stimulation can have effects on PH, flow rate, affecting ion trapping

## Slide 10: Oral fluid testing
Advantages
  Less invasive, observed collection
  Training important but clinical expertise not required
  Difficult to adulterate
  Gender neutral specimen collection
  Basic drugs concentrate in lower Ph of oral fluid
  Oral or inhaled drugs coat the oral mucosa

## Slide 11: Oral fluid testing
Limitations
  Specimen volume
  Drug absorption to the collection device
  Elution buffer critically important
    Drug recovery
    Drug stabilization
    Dilutes the OF
    May interfere with analytical techniques

## Slide 12: Drugs in OF
mechanisms affected by:
  Molecular size
  % protein bound in blood
  Lipophilicity of drug
    Non-polar analytes partition into OF more readily than polar metabolites – higher parent drug concentrations
  Pka of drug
    Non-ionized basic drugs in blood partition into more acidic OF – ion trapping of basic drugs
  Passive diffusion of free unchanged drug, ultrafiltration (alcohol), active secretion & coating of oral mucosa from smoked, inhaled, insufflated drugs

## Slide 13: Factors affecting drugs in OF
Physiochemical characteristics
Route of drug administration
Biological matrix attributes (PH)
Drug dose
Physiological factors
Analytical method capabilities
Time factors
Specimen collection
Drug and metabolite stability
Individual variability

## Slide 14: Hair Drug Testing

## Slide 15: Introduction
Drugs circulating in the blood get incorporated into the hair cells
Drugs are then trapped when the hair is keratinized
The trapped drug then moves out on the hair as it grows
In theory, this creates a calendar of previous drug use
In reality, it is more complicated
  Drugs can be deposited from sweat, and secretions as well as external sources (powders, smoke)

## Slide 16: Hair analysis
Analysis is straightforward
Interpretation the challenge
SoHT – Society of Hair Testing – 1995

## Slide 17: Applications
Drug –related deaths
Drug-facilitated crimes
Child protection cases
Drug use monitoring
  Workplace
  Rehabilitation
  Driver’s license reinstatement

## Slide 18: Hair physiology
Composed of proteins (65-95%), lipids (1-9%) pigments (0.1-5%)
Minor amounts of trace elements, polysaccharides and water
Cuticle – a sheath of overlapping scale cells
Cortex – the bulk of the hair fiber
  Spindle shaped keratin-containing cells
Medulla – center of the cortex
  Can be continuous or fragmented
Hair is formed in the follicle 3-5mm
beneath the epidermis

## Slide 19: Hair Physiology
During formation melanin pigments are introduced into the hair
Melanin is only a few percent of the hair matrix
  Attract and bind chemicals
Growth rate is a factor for interpretation and incorporation

## Slide 20: Drug Disposition into the Hair
Active or passive diffusion from the blood vessels in the dermal papilla
Diffusion from sweat and other secretions bathing the growing or mature hair
External drugs from vapor or solid that diffuse into the mature hair

## Slide 21: Systematic Incorporation from the Blood
Rapid cell division requires good blood supply to the hair follicle and results in the ready delivery of circulating drug molecules to the growing hair.
For drugs to enter the matrix they need to diffuse across the cell membrane
Rate is dependent on the lipid solubility of the drug, pH between the blood and cell
Once in the cell cytosol, the molecule will be protonated and not able to diffuse back to the blood

## Slide 22: Incorporation from Sweat and Other Secretions
Administered drugs or metabolites will excrete in sweat or sebum and therefore are potential routes for drug incorporation into the hair.
Drugs like codeine and cocaine can be detected in hair shortly after administration, suggesting deposition on the already mature hair.
Deposition from sweat come from consumed drugs
  Problematic if comes from someone else’s sweat

## Slide 23: Incorporation from External Contamination
Exposure of hair to environment, external contamination should be considered an alternative explanation for a positive result.
Some drugs can be removed by washing and others not.

## Slide 25: Drug Analysis
Segmentation
Washing
Homogeneity and sample amount
Extraction

## Slide 26: Benefits and drawbacks of hair
Historical
Analysis
Orientation
  identify the root
Not current snapshot

## Slide 27: testing types
screening
Multi-drug screen test cup
Cassette
Dip Card
Drug strips
Chromatographic analysis
Spectral identifications
Confirmatory

## Slide 28: Drug testing

## Slide 29: Screening test
6-monoacetylmorphine
Amphetamine
Barbiturates
Buprenorphine
Benzodiazepines
Clonazepam
Cocaine
Cotinine
Methadone metabolite
Ethyglucuronide
Norfentanyl
Synthetic marijuana
AB-PINACA
Mitragynine
Ecstacy
Methamphetamine
Methadone
Morphine
Opiates
Oxycodone
Phencyclidine
Tricyclic antidepressants
Marijuana
Tramadol

## Slide 30: Drug testing
More than one test
Screening or preliminary testing
Confirmatory testing
Understand the scope and limitations of the testing choice

## Slide 31: Testing limitations
What does it detect well
What does it not detect well
Studies done under optimal conditions
Did not evaluate for drug-drug interactions

## Slide 32: 6-monoacetylmorphine
Why important?
Detect well:
6AM
Does not detect well:
Morphine, heroin, codeine, oxycodone, oxymorphone

## Slide 33: amphetamine
Why important?
Detect well:
amphetamine
Does not detect well:
MDA, phentermine, methamphetamine

## Slide 34: Cocaine
Why important?
Does detect well:
Benzoylecgonine
Does not detect well:
Cocaine
Cocaethylene
Ecgonine

## Slide 35: Fentanyl
Why important?
Does detect well:
Norfentanyl
Does not detect well:
Fentanyl
No mention of fentanyl analogs

## Slide 36: THC
Why important?
Does detect well:
11-nor-9-carboxy THC
Does not detect well:
Delta-9-THC
Delta-8-THC
Cannabidiol
Cannabinol
11-OH THC

## Slide 37: What’s missing?
Unknown unknowns

## Slide 38: Analytical instrumentation
Liquid chromatography – mass spectrometry
Gas chromatography – mass spectrometry
Liquid chromatography – quadrupole-time of flight
Separation of the mixture, isolation of the analyte for identification
Be mindful of the scope

## Slide 39: NDEWS

## Slide 41: Breaking news, or not…
Increasing conversation:
  Tucibi, 2c-B, pink cocaine, C, 2C, tuci
    Rarely contains 2C compounds
    MDMA, ketamine, caffeine, “bath salts”, fentanyl, and/or other opioids
    Rave-type settings
  2-MMC, 2-Methylmethcathinone
    substituted cathinone derivative
    related to 3-methylmethcathinone and 4-methylmethcathinone (mephedrone).
    stimulant and euphoric effects.

## Slide 42
Kratom
Nitazenes, Isotonitazene, Brorphine, Metonitizine, Protonitizine, N-Pyrrolidino Protonitazene, N-Pyrrolidino Metonitazene
  Increased potency compared to fentanyl
  ‘des’ compounds don’t react with testing strips
  Mixed with other analytes
Avizafone
  Prodrug for diazepam

## Slide 43
Cyclorphine
  a "benzimidazolone derivative
  potent opioid effects
  around 4 times stronger than fentanyl
  Heavily sedating

## Slide 44
Fentanyl
  Fatalities decreasing
  Present in 50% of heroin cases
  Increasing prevalence in stimulants (Meth, coc)
  Co-occurrence with others (prescription benzos, cannabinoids, hallucinogens, prescription stims)

## Slide 46: Congratulations!
There are so many working to lower that number and you are to be commended

## Slide 47: Answers to questions
Thank you!